## Slide 1: Testing Chapter 7

## Slide 2: Motivation
Development is accompanied by “bugs.”
Catching bugs early saves money
  The further a bug progresses the more impact it has on the system
    A bug fix requires all related modules to be retested.
    A bug fix may require redesigning related modules.
  For example
    PCB design flaw
    VLSI layout error
    Subtle coding flaw
Testing doesn’t remove bugs, it just makes it less likely they exist.

## Slide 3: Testing Principles
Testing proceeds with design process
  Write tests while designing modules
  Perform tests while implementing modules
The Test-Vee illustrates this process

## Slide 4: Developing Test Cases The Rationale
Test cases define exactly what the module must do.
Testing prevents feature creep, since the development of a module is complete when its test is passed.
Test cases motivate developers by providing immediate feedback.
Test cases force designers to think about extreme cases.
Test cases are a form of documentation.
Test cases force the designer to consider the design of the module before building it.

## Slide 5: Testing
Quality design documents
  Requires you to reason about system behavior
  Gives your design clear goals
  Enables you to look at your system from the tester’s perspective
How should we perform testing?
  Tradeoff
    Apply every possible input, or
    Apply selected inputs which might yield errors
  Test should be chosen to increase likelihood of finding an error.

## Slide 6: Types of Testing
Black box testing
  No knowledge of internal organization
  Only access input and outputs
  Change inputs and observe outputs
White box testing
  Knowledge of internal organization
  Might have expectation of fault model
  Create test instances which reveal physical or logical errors
Gray box Testing (relevant for software testing)
  Combination of black box and white box testing

## Slide 7: Black-, Gray-, & White-Box Testing
Black box
… requirements
Actual output
compared
with
required output
White box
Gray box
… requirements &
key design elements
Input determined by
Result
…design
elements
Confirmation
of expected
behavior
As for black- and white box testing
Adapted from Software Engineering: An Object-Oriented Perspective by Eric J. Braude (Wiley 2001), with permission.

## Slide 8: Black-box Testing

## Slide 9: White Box Testing – Software Paths to be Checked
Parameter & settings make
sense?
Parameter name too long?
N
Y
N
Decision Coverage
Set _name to
“defaultName"
Y
Truncate
name
Set _name
to parameter
Adapted from Software Engineering: An Object-Oriented Perspective by Eric J. Braude (Wiley 2001), with permission.
The objective of path testing is to ensure that the set of test cases is such that each path through the program is executed at least once.

## Slide 10: Design for Testability
A major goal in engineering is to design systems with high testability.
A testable design is easier to
  Debug
    If a design is “testable” then a failure of a component can be
      Quickly detected
      Quickly located
  Manufacture, and
  Service in the field
Design with high testability is possible if both the “Controllability” and “Observability” of system are also high.
Controllability
  When any node of the system can be accessed to set the associated variable of interest (i.e. voltage) to a desired value
Observability
  When measurements of interest can be made at any node of the system.

## Slide 11: Stubs for Testing
A placeholder for future functionality
A device which mimics subsystem
  Simulates input or monitors outputs
  For a unit under test (UUT)
  Insure good behavior
    before wreaking havoc on the rest of the system
Examples of A Stub:
  A function generator for an audio input
  A printf() instead of a file write
  DIP switch instead of a bus connection

## Slide 12: Stub A Hardware Example

## Slide 13: Stubs (and Drivers) Isolating the Module UUT
Driver
Stub
Stub
Stub
Module to
Test
Test
cases
Results

## Slide 14: Test Case Properties
Accurate - The test should check what it is supposed to and exercise an area of intent.
Economical - The test should be performed in a minimal number of steps.
Limited in complexity - Tests should consist of a moderate number (10-15) of steps.
Repeatable - The test should be able to be performed and repeated by another person.
Appropriate - The complexity of the test should be such that it is able to be performed by other individuals who are assigned the testing task.
Traceable - The test should verify a specific requirement.
Self cleaning - The system should return to the pre-test state after the test is complete.

## Slide 15: Constructing Tests
There are many types of testing and several taxonomies to classify testing procedures or methodologies.
We will focus on four types as
Debugging
Unit Testing
Integration Testing
Acceptance Testing

## Slide 16: Debugging
There are two types of bugs:
Bohrbugs
  Bohrbugs are reliable bugs
  The error is always in the same place and the same way
    Example: accessing the incorrrect element of an array
    Example: incorrect connection for a logic gate input
  Solution: set a good trap that causes the associated error, and reveals the source of error.
Heisenbugs
  Innocuous changes of input yield buggy behavior
  May not be reproducible
  They seemingly move around within a system
    Example: a pointer error that occasionally writes the system stack!
    Example: a circuit that operates incorrectly at random times (a floating ground line?)
  Solution: not trivial, must think outside the box!

## Slide 17: Debugging Process
Observe the problem under different operating conditions
Form a hypothesis as to what the potential problem is
Conduct experiments to confirm or eliminate the hypothesized source of the problem
Repeat until the problem is eliminated

## Slide 18: Debugging Common Problems
Check easiest problems first
  You can perform more in a given time
Start at lowest levels of abstraction
  Upper levels rely on lower level
Examples
  Is the system powered up?
  Is the testing equipment adjusted properly?
  Are the bus lines being correctly manipulated?
  Have you initialized the system?
  Are you printing out the right variable/type?

## Slide 19: Unit Testing
A unit test is a COMPLETE test of the functionality of a system module in isolation.
Should be traceable to the detailed design.
Consists of a set of test cases.
Each test case establishes that a subsystem performs a single unit of functionality to some specification.
Test cases should be written with the express intent of uncovering undiscovered defects.

## Slide 20: Unit Testing Example Robot Electro-mechanical Architecture

## Slide 21: Unit Testing Qualifying Subsystems or Modules
MCU (hardware)
LCD
Switches
Digital Compass
Range finder
H-bridge
Motors
Chassis
MCU (software)

## Slide 22: Unit Test: The Digital Compass Functional Requirements
Module | Digital Compass – Geosensor version 2.3
Inputs | Earth’s magnetic field: An orientated field of magnetic force beginning and ending at the earth’s magnetic poles. SClk – Clock signal to clock data through the module. Maximum Frequency is 10Mhz. SDIn – Serial data input to send data into the compass module. Date is valid on positive SClk edges.
Outputs | SDOut – Serial data output from the compass module. Data is valid on negative clock edges.
Functionality | Senses the earth’s magnetic field and determines the orientation of the compass with respect to the field. This orientation is stored in an internal register and can be retrieved through the SPI interface.
Test | Comp-UT-01

## Slide 23: Unit Test: The Digital Compass Matrix Test
Test Writer: Sue L. Engineer |  |  |  |  |  |  |  | 
 | Test Case Name: | Compass unit test #1 |  |  |  |  | Test ID #: | Comp-UT-01
 | Description: | Checks that the compass returns correct angular measurements to the MCU. Test program is in ./test/compass_unit_test_1.c |  |  |  |  | Type: |  white box  black box
Tester Information |  |  |  |  |  |  |  | 
 | Name of Tester: |  |  |  |  |  | Date: | 
 | Hardware Ver: | Compass Module - Geosensor version 2.3 |  |  |  |  | Time: | 
 | Setup: | Compass module should be wired to the MCU through the SPI interface pins. The MCU should be connected to an RS232 terminal through its SCI interface. The terminal should be configured to run at 9600 baud. Cardinal directions map should be aligned using the magnetic compass. |  |  |  |  |  | 
Step | Action | Expected Result | Pass | Fail | N/A | Comments |  | 
1 | Compile compass.c in /test directory | IDE should generate no warnings or errors. |  |  |  |  |  | 
2 | Download | MCU should report “download successful” |  |  |  |  |  | 
3 | Execute | MCU should display compass splash screen on terminal interface. |  |  |  |  |  | 
4 | Orientate compass to 0 degrees. | Terminal interface should display 0 degrees +/- 10 degrees. |  |  |  |  |  | 
5 | Orientate compass to 30 degrees. | Terminal interface should display 30 degrees +/- 10 degrees. |  |  |  |  |  | 
6 | Orientate compass to 45 degrees. | Terminal interface should display 45 degrees +/- 10 degrees. |  |  |  |  |  | 
… | … | … |  |  |  |  |  | 
12 | Orientate compass to 315degrees. | Terminal interface should display 315 degrees +/- 10 degrees. |  |  |  |  |  | 
 | Overall test result: |  |  |  |  |  |  | 

## Slide 24: Unit Testing Methods
Matrix Test
Automated Scripts Tests
Step-by-step Test
Note: these can be applied to any level of test: unit, integration, acceptance, etc.

## Slide 25: Matrix Test
Appropriate for cases where the inputs are structurally the same and differ only in their values.
Consider a test for the analog-to-digital (ADC) (temperature measurement system).
Assuming that ADC’s clock frequency is 10 KHz and the input ranges from 0 to 5 V.
The Unit Test will entail applying different inputs to the ADC and verifying the outputs.
The applicable text matrix is presented next.

## Slide 26: Matrix Test Test Template for ADC
Test Writer: Sue L. Engineer |  |  |  |  |  |  |  |  |  | 
 | Test Case Name: |  |  | ADC unit test |  |  | Test ID #: |  |  | ADC-UT-01
 | Description: |  |  | Verify conversion range and clock frequency. Output goes to 0 in presence of null clock. |  |  | Type: |  |  |  white box  black box
Tester Information |  |  |  |  |  |  |  |  |  | 
 |  | Name of Tester: |  |  |  |  | Date: |  |  | 
 |  | Hardware Ver: |  | 1.0 |  |  | Time: |  |  | 
 |  | Setup: |  | Isolate the ADC from the system by removing configuration jumpers. Connect the CLK input to 10 KHz clock source and the Din input to a high-precision voltage source. Connect the output from the ADC to a logic analyzer. |  |  |  |  |  | 
Test |  | VT | Clock |  | Expected output |  | Pass | Fail | N/A | Comments
 |  |  |  |  | Decimal | Hexadecimal |  |  |  | 
1 |  | 0.0V | 10 KHz |  | 0 | 0x000 |  |  |  | 
2 |  | 2.0 V | 0 Hz |  | 0 | 0x000 |  |  |  | 
10 |  | 2.502 V | 10 KHz |  | 512 | 0x200 |  |  |  | 
 |  | Overall test result: |  |  |  |  |  |  |  | 

## Slide 27: Unit Testing Step-by-Step Tests
A step-by-step test case follows a prescribed approach to generate the test and checking the results.
  Appropriate for complex test cases.
The test template has an additional column in comparison the same for the Matrix Test.
  Specific action the tester must perform at each step in the test process is defined in that column.
Consider the vending machine state diagram that accepts nickels and dimes and dispenses candy when total is $0.25 (or more).
  Its state machine has multiple processing paths.
  A test case can be written for each processing path.

## Slide 28: Unit Testing Step-by-Step Test for Vending
Test Writer: Sue L. Engineer |  |  |  |  |  |  |  | 
 | Test Case Name: | Finite State Machine Path Test #1 |  |  |  |  | Test ID #: | FSM-Path-01
 | Description: | Simulate insertion of money with a mix of nickels and dimes. Verifies FSM, outputs candy in response to a total deposit of $0.25. |  |  |  |  | Type: |  white box  black box
Tester Information |  |  |  |  |  |  |  | 
 | Name of Tester: |  |  |  |  |  | Date: | 
 | Hardware Ver: | 1.0 |  |  |  |  | Time: | 
 | Setup: | Make sure that the system was reset sometime prior and is in state $0.00. |  |  |  |  |  | 
Step | Action | Expected Result | Pass | Fail | N/A | Comments |  | 
1 | Strobe Nickel | State should go to $0.05 |  |  |  |  |  | 
2 | Strobe Dime | State should go to $0.15 |  |  |  |  |  | 
3 | Wait | State should remain $0.15 |  |  |  |  |  | 
4 | Strobe Nickel | State should go to $0.20 |  |  |  |  |  | 
5 | Strobe Dime | State should go to $0.25 |  |  |  |  |  | 
6 | Nothing | State should go to $0.00 |  |  |  |  |  | 
 | Overall test result: |  |  |  |  |  |  | 

## Slide 29: Unit Testing Automated Test Scripts
A sequence of commands provided to the UUT to facilitate testing without human intervention.
  The generated outputs can be compared to expected outputs to determine if there is an error: this can be automated as well.
Useful for regression testing phase
  The process of retesting a module after a modification to make sure no new errors were introduced.
Developing testing scripts require significant up-front cost.

## Slide 30: Complete Testing Process for Software Illustrated

## Slide 31: Integration Testing
Checks that major modules work correctly.
Write the integration test during Level 1 design:
  Help insure requirements are being met.
  Help to firm-up design
  Requires the designer think about the expected behavior of the subsystems.
  Requires designer to think about extreme behaviors of subsystems.

## Slide 32: Integration Testing Formulation of Test Cases
Following questions can be the bases for formulating the test cases:
What are the different paths of execution through the system?
Are all modules exercised at least once during integration testing?
Have all the interface signals been tested?
Have all the interface modes been exercised?
Does the system process information at the required rate and meet timing requirements?

## Slide 33: Integration Testing Software Design Perspective
The entire system is viewed as a collection of subsystems (sets of classes) determined during the system and object design.
The order in which the subsystems are selected for testing and integration determines the testing strategy
  Big bang integration (Non-incremental)
  Bottom up integration
  Top down integration
  Sandwich testing
  Variations of the above

## Slide 34: Integration Testing Software Example: Three Layer Call Hierarchy
A
B
C
D
G
F
E
Layer I
Layer II
Layer III

## Slide 35: Integration Testing Big-Bang Approach
Unit Test
F
Unit Test
E
Unit Test
D
Unit Test
C
Unit Test
B
Unit Test
A
System Test
Don’t try this!

## Slide 36: Integration Testing Bottom-Up
A
B
C
D
G
F
E
Layer I
Layer II
Layer III
Test F
Test E
Test G
Test C
Test D,G
Test B, E, F
Test
A, B, C, D,
E, F, G
Special program needed to do the testing, namely a “Test Driver”: A routine that calls a subsystem and passes a test case to it.

## Slide 37: Integration Testing Pros and Cons of Bottom-Up
Bad for functionally decomposed systems:
  Tests the most important subsystem (UI) last
Useful for integrating the following systems
  Object-oriented systems
  real-time systems
  systems with strict performance requirements

## Slide 38: Integration Testing Top-Down Methodology
A
B
C
D
G
F
E
Layer I
Layer II
Layer III
Test A
Layer I
Test A, B, C, D
Layer I + II
Test
A, B, C, D,
E, F, G
All Layers
Special program is needed to do the testing, Test Stub:
  A program or a method that simulates the activity of a missing subsystem by answering to the calling sequence of the calling subsystem and returning back fake data.

## Slide 39: Integration Testing Pros and Cons of Top-Down
Test cases can be defined in terms of the functionality of the system (functional requirements)
Writing stubs can be difficult: Stubs must allow all possible conditions to be tested.
Possibly a very large number of stubs may be required, especially if the lowest level of the system contains many modules/methods.
One solution to avoid too many stubs: Modified top-down testing strategy
  Test each layer of the system decomposition individually before merging the layers
  Disadvantage of modified top-down testing: Both, stubs and drivers are needed

## Slide 40: Integration Testing Sandwich Testing Strategy
Combines top-down strategy with bottom-up strategy
The system is viewed as having three layers
  A target layer in the middle
  A layer above the target
  A layer below the target
  Testing converges at the target layer
How do you select the target layer if there are more than 3 layers?
  Heuristic: Try to minimize the number of stubs and drivers

## Slide 41: Integration Testing Sandwich Testing Strategy
A
B
C
D
G
F
E
Layer I
Layer II
Layer III
Test E
Test D,G
Test B, E, F
Test
A, B, C, D,
E, F, G
Test F
Test G
Test A
Bottom
Layer
Tests
Top
Layer
Tests
Test A,B,C, D
up
down

## Slide 42: Integration Testing Pros and Cons of Sandwich Testing
Top and Bottom Layer Tests can be done in parallel
Does not test the individual subsystems thoroughly before integration.

## Slide 43: Integration Testing Possibilities
MCU + motors + bridge + switches
Chassis + digital compass + MCU + motors + bridge +LCD
Chassis + range finder + MCU + motors + bridge

## Slide 44: Integration Testing Step-by-Step Testing
Test Writer: Sue L. Engineer |  |  |  |  |  |  |  | 
 | Test Case Name: | Robot integration test #1 |  |  |  |  | Test ID #: | Robot-IT-01
 | Description: | Checks interaction of DC motors on the magnetic compass. |  |  |  |  | Type: |  white box  black box
Tester Information |  |  |  |  |  |  |  | 
 | Name of Tester: |  |  |  |  |  | Date: | 
 | Hardware Ver: | Robot 1.0 |  |  |  |  | Time: | 
 | Setup: | A wooden turn-table should be placed on top of the cardinal direction map. This map should be aligned with a magnetic compass. There should be no metal present while the alignment is being performed. Next, the partially assembled robot should be placed on the turn-table. The MCU should be connected to a terminal to observe and record data. |  |  |  |  |  | 
Step | Action | Expected Result | Pass | Fail | N/A | Comments |  | 
1 | Write program to spool compass readings while simultaneously driving motors. | Program should be statically tested to verify accuracy. Should sample compass at a sufficient rate depending on speed. |  |  |  |  |  | 
2 | Run acceptance test | Test program should prompt user to turn the robot to an orientation and then spin the motors will then spin up and down. |  |  |  |  |  | 
3 | Plot spooled data in spreadsheet program. | Plots should be analyzed to see if compass deviated any more than 10 degrees from set point. |  |  |  |  |  | 
 | Overall test result: |  |  |  |  |  |  | 

## Slide 45: System Testing
There are 5 stages for System Testing:
Functional Testing
Structure Testing
Performance Testing
Acceptance Testing
Installation Testing
Impact of requirements on system testing:
The more explicit the requirements, the easier they are to test.
Quality of use cases determines the ease of functional testing
Quality of subsystem decomposition determines the ease of structure testing
Quality of nonfunctional requirements and constraints determines the ease of performance tests.

## Slide 46: Structure Testing
Essentially the same as white box testing.
Goal: Cover all paths in the system design
Self reading

## Slide 47: Functional Testing
Essentially the same as black box testing
Goal: Test functionality of system
Test cases are designed from the requirements analysis document (better: user manual) and centered around requirements and key functions (use cases)
.
.

## Slide 48: Performance Testing
Timing testing
  Evaluate response times and time to perform a function
Environmental testing
  Test tolerances for heat, humidity, motion, portability
Quality testing
  Test reliability, maintain- ability & availability of the system
Recovery testing
  Tests system’s response to presence of errors or loss of data.
Human factors testing
  Tests user interface with user
Stress Testing
  Stress limits of system (maximum # of users, peak demands, extended operation)
Volume testing
  Test what happens if large amounts of data are handled
Configuration testing
  Test the various software and hardware configurations
Compatibility testing
  Test backward compatibility with existing systems
Security testing
  Try to violate security requirements

## Slide 49: Acceptance Testing
Might be formal legal document
Written along with requirements
Traceable to engineering requirements
Identifies
  Scope – how much of the system is tested?
  Level – how deep will testing be performed?

## Slide 50: Acceptance Testing Software Design Perspective
Goal: Demonstrate system is ready for operational use
  Choice of tests is made by client/sponsor
  Many tests can be taken from integration testing
  Acceptance test is performed by the client, not by the developer.
Majority of all bugs in software is typically found by the client after the system is in use, not by the developers or testers. Therefore two kinds of additional tests:
Alpha test:
  Sponsor uses the software at the developer’s site.
  Software used in a controlled setting, with the developer always ready to fix bugs.
Beta test:
  Conducted at sponsor’s site (developer is not present)
  Software gets a realistic workout in target environ- ment
  Potential customer might get discouraged

## Slide 51: Application: Autonomous Robot
Autonomous navigating robot
Engineering requirements
  The robot’s center must stay within 12 to 18 centimeters of the wall over 90% of the course, while traveling parallel to a wall over a 3 meter course.
  The robot’s heading should never deviate no more than 10 degrees from the wall’s axis, while traveling parallel to a straight wall over a 3 meter course.

## Slide 52: Acceptance Test Robot
Test Writer: Sue L. Engineer |  |  |  |  |  |  |  | 
 | Test Case Name: | Robot acceptance test #1 |  |  |  |  | Test ID #: | Robot-AT-01
 | Description: | Checks the engineering requirement: The robot’s center must stay within 12 to 18 centimeters of the wall over 90% of the course, while traveling parallel to a wall over a 3 meter course. |  |  |  |  | Type: |  white box  black box
Tester Information |  |  |  |  |  |  |  | 
 | Name of Tester: |  |  |  |  |  | Date: | 
 | Hardware Ver: | Robot 1.0 |  |  |  |  | Time: | 
 | Setup: | Completed robot should be fully charged and placed on 3 meter test track. |  |  |  |  |  | 
Step | Action | Expected Result | Pass | Fail | N/A | Comments |  | 
1 | Write a program to monitor the robot’s position from the wall. | Program should be statically tested to verify accuracy. Should sample wall at a sufficient rate depending on speed. |  |  |  |  |  | 
2 | Put robot on test track, run test, and download data. | The robot should travel down the entire length of the test track and then stop. |  |  |  |  |  | 
3 | Plot test data in a spreadsheet program. | Plot of position vs. time should be within 12 – 18 cm 90% of the time. |  |  |  |  |  | 
 | Overall test result: |  |  |  |  |  |  | 

## Slide 53: Testing has its Own Life Cycle
Establish the test objectives
Design the test cases
Write the test cases
Test the test cases
Execute the tests
Evaluate the test results
Change the system
Do regression testing

## Slide 54: Test Team
Test
Analyst
Team
User
Programmer
too familiar
with code
Professional
Tester
Configuration
Management
Specialist
System
Designer
Albert Einstein –”We can't solve problems by using the same kind of thinking we used when we created them.”

## Slide 55: Conclusion on Testing
Reasons to develop and conduct tests
Testing reduces the number of bugs in existing and new features.
Tests are good documentation.
Tests improve design.
Tests allow you to redesign.
Tests constrain features.
Tests defend against other designers.
Testing is fun.
Testing forces you to slow down and think.
Testing makes development faster.
Tests reduce fear.